## Slide 1: Wireless Team
Advisor: Haitham Afifi
Chethan Lokesh Mariyaklla
Pavitra Basappa Gudimani
Priyanka Giri

## Slide 2: Problem Statement & Solution
Problem Statement
  Wireless transmission in a network with multiple collision domains and defect nodes
Solution
  DRL agent is used to route packets from source to destination by avoiding collisions and defect nodes in wireless networks

## Slide 3: Wireless Network
Range 1
Range 2

## Slide 4: Challenges in Wireless Networks
1. Interference

## Slide 5: Challenges in Wireless Networks
2. Hidden terminal problem

## Slide 6: Challenges in Wireless Networks
3. Defect node in routing path
Destination: Node 6
Source: Node 1
Defect Node
Packet Dropped

## Slide 7: Network Topology
Smaller network
  2 collision domains
  6 nodes
Larger network
  6 collision domains
  11 nodes

## Slide 8: Centralized - State, Action and Rewards
State
  Destination of a packet at each node
  Defect node
  State space for 6 nodes
    MultiDiscrete ( [7, 7, 7, 7, 7, 7, 6] )
Action
  Next hop of each node within range and transmit/wait (T/W) status
  Action space for 6 nodes
    MultiDiscrete ( [4, 4, 6, 6, 4, 4] )
    Example - [1, 1, 2, 3, 4, 5] = [T, W, W, W, W, W]

## Slide 9: Centralized - State, Action and Rewards
Rewards
  Transmission of packet
    Collision (-1)
    Transmit to defect node (-1)
    Packet reaching destination (+1)
  Routing
    - (Hop_count * 0.01)

## Slide 10: Baseline
Destination Sequenced Distance Vector (DSDV) with TDMA

## Slide 11: Training Results
Smaller network with dynamic defect node
Reward convergence graph
Timesteps

## Slide 12: Training Results
Smaller network with dynamic defect node
Packet loss graph (Total 25 packets)
Timesteps

## Slide 13: Evaluation
PPO2 Vs A2C

## Slide 14: Evaluation
Baseline Vs PPO2

## Slide 15: Work in Progress – Decentralized Network
Decentralized wireless network
  Each node acts as a agent

## Slide 16: Decentralized - State, Action and Rewards
State
  Destination of a packet at each node
  Queue status
  Defect node
  State space for each 6 nodes
    MultiDiscrete ( [7, 7, 7, 7, 7, 7, 30, 30, 30, 30, 30, 30, 6] )
Action
  Next hop of each node within range and transmit/wait (T/W) status
  Action space for each node
    {0:[4],1:[4], 2:[6], 3:[6], 4:[4], 5:[5]}

## Slide 17: Decentralized - State, Action and Rewards
Rewards
  Transmission of packet
    Collision (-1)
    Transmit to defect node (-1)
    Packet reaching destination (+1)
  Routing
    - (Hop_count * 0.01)

## Slide 18: Decentralized Network Results
Smaller network without fault node
Reward convergence graph
Timesteps

## Slide 19: Challenges Faced
Tuning

## Slide 20: References
[1]. X. Guo, H. Lin, Z. Li and M. Peng, "Deep reinforcement learning based qos-aware secure routing for sdn-iot", IEEE Internet of Things Journal, 2019.
[2]. Yiding Yu, Taotao Wang, Soung Chang Liew, "Deep-Reinforcement Learning Multiple Access for Heterogeneous Wireless Networks", Selected Areas in Communications IEEE Journal on, 2019.

## Slide 21
THANK YOU!